## Slide 1: IDS Escape Game
buildingSMART Belgium

## Slide 2: Introduction IDS
https://github.com/buildingSMART/IDS/tree/development/Documentation/UserManual
© buildingSMART International – IDS User Manual (GitHub), CC BY-ND 4.0.

## Slide 3: Information Delivery Specification (IDS)
buildingSMART standard for defining information requirements in a computer-interpretable form.
    It enables automatic checks of IFC models, which increases quality assurance and data reliability. IDS also supports efficient delivery of the data by setting expectations and providing clear guidance on what needs to be exchanged. An IDS user can specify how objects, classifications, materials, properties and even values should be provided in an IFC model.

## Slide 4: IDS example
© buildingSMART International, CC BY-ND 4.0.

## Slide 5: IDS and IFC
IDS is strictly linked to the IFC data schema. It allows for unambiguous interpretation and automatic checks, with all controlling software producing identical results.
Supported IFC schemes:
IFC4X3_ADD2
IFC4
IFC2X3

## Slide 6: Goal IDS
  The IDS specification has two core tasks
      recording appointments checking compliance
  It is recommended to start with an IDS before data production starts, this ensures clear guidelines for data production, preventing incorrect input.
CHECKING
SPECIFYING

## Slide 7: Purpose IDS
      IDS is limited to alphanumeric information:
      Values of properties Quantities Classifications Materials Relationships
  but it does not cover geometric aspects
Notes: Specificeren en controleren
Geen effectieve inhoudcontrole

## Slide 8: What is IDS not for?
      detecting clashes, such as collisions between beams and pipes checking geometric distances, such as walls that must be at least 3 m from the plot boundary performing calculations or aggregations, such as determining whether the total office area is greater than 300 m² enforcing uniqueness across multiple objects, such as unique names for all door types assessing performance or software behavior, such as model load times validating external or linked data, such as drawings and revisions in a CDE checking whether a model corresponds to the as-built condition of the execution

## Slide 9: IDS <> bSDD
Both intended to record agreements about data content. The bSDD can be seen as a shared library of properties that can be applied when creating an IDS. Thanks to this synergy, we encourage the use of consistent terms across the industry.

## Slide 10: IDS <> ISO 19650
5.2.1 Establish the appointing party’s exchange information requirements
5.4.3 Establish the lead appointed party’s exchange information requirements
5.6.3 Undertake quality assurance check
5.6.4 Review information and approve for sharing
5.6.5 Information model review
5.7.2 Review and authorize the information model
5.7.4 Review and accept the information model
CHECKING
SPECIFYING

## Slide 11: IDS proces

## Slide 12: IDS software
Specifying
IDS Maker (BIM vision)
BIMcollab Nexus
usBIM.IDS editor (ACCA)
IDS editor (Solibri)
IDS Learn
IDSedit – ISD Spec Editor
…
Checking
IDS Checker (BIM vision)
BIMcollab Zoom
usBIM.IDS validator (ACCA)
Solibri Office
Bonsai BIM
Qonic
…
Paying (trail possible) Free starter version

## Slide 17: IDS Structure
    Each IDS file can be described with metadata and can contain one or more specifications.
Human readable
Machine readable
© buildingSMART International – IDS User Manual (GitHub), CC BY-ND 4.0.

## Slide 18: IDS Structure | Specification metadata
Serves to describe the purpose, intentions and usefulness of these Specifications for the recipients of the IDS:
      why information is needed who will benefit when it will be used.
This helps to ensure that the requirements are effectively adhered to.

## Slide 20
© buildingSMART International – IDS User Manual (GitHub), CC BY-ND 4.0.

## Slide 21: IDS Structure | Specifications
Specifications consist of two parts:
      Applicability
      Identifies the subset of the model that we are intending to specify.
      It identifies the subset of the model to which the Specification should be applied. This subset can be determined using the available facets, such as entity (e.g., walls, windows), classification, and others.
      Requirements
      Specifies what these elements should or should not have.
      It describes which information is required for the subset defined in the Applicability, such as mandatory properties or materials.

## Slide 22: IDS Structure | Facets
Applicability and Requirements are described using a collection Facets.
    A Facet describes its information precisely using fixed Facet Parameters so that computers can understand exactly what information you are after.
Facets
Facet Parameters

## Slide 23: IDS Structure | Facets
© buildingSMART International – IDS User Manual (GitHub), CC BY-ND 4.0.
There are six different Facets of information:

## Slide 24: IDS Structure | Facet Parts
    This facet either identifies objects that are part-of another (applicability), or require that they are (requirement), in particular the relationships.
      The IFCRELAGGREGATES relationship describes how multiple smaller sub-objects can be aggregated into a single bigger object
      The IFCRELASSIGNSTOGROUP relationship describes how multiple objects can be grouped into a collection of objects any use-case
      The IFCRELCONTAINEDINSPATIALSTRUCTURE relationship describes how multiple objects can be located in a particular location
      The IFCRELNESTS relationship describes how a physical object may be connected to a larger host object, typically through a physical connection such as a pre-drilled hole or connection terminal. When the host moves, the attached nested objects move with it.
      The IFCRELVOIDSELEMENT relationship describes how a void belongs to an element.
      The IFCRELFILLSELEMENT relationship describes how an element fills a void, making it part of the void.

## Slide 25: IDS Structure | Facet Parameters
    The Facet parameters are specified based on either a Simple Value or a Complex Restriction.
Simple Value
      Text
      Number
      Boolean (TRUE / FALSE)
Complex Restriction
      Enumeration [bSDD]
      Pattern [Regex]
      Bounds
      Length

## Slide 26: IDS Structure | Complex Restrictions
      A list of valid values A range of numbers Specify a text pattern
For example: to specify that a fire resistance property must only have one of the following values: "REI30", "REI60" or "REI120".

## Slide 27: IDS Structure | Complex Restrictions
      A list of valid values A range of numbers Specify a text pattern
For example: to specify that naming must comply with a naming standard
Regex - Regex Generator

## Slide 28: IDS Structure | Cardinality
    Cardinality can be set within both the Applicability and the Requirements with one of the following values:
      required
      optional
      prohibed
Notes: Cardinality geeft aan of een facet (eigenschap, relatie of object) moet, mag of niet mag voorkomen binnen de scope van een IDS-regel (applicability of requirement).
Cardinality bepaalt of iets verplicht, optioneel, meervoudig of verboden is.

## Slide 29: IDS Structure | Cardinality
Applicability
At least one object according to the determined applicability must exist For example, there must be one reference object that defines the zero point.
© buildingSMART International – IDS User Manual (GitHub), CC BY-ND 4.0.
Notes: Verschillende per software: Solibri geeft een non-conformiteit, terwijl Blender aangeeft dit te hebben overgeslaan.

## Slide 30: IDS Structure | Cardinality
Applicability
An object according to the determined applicability may exist For example: IfcGrid may be present in the model, but is not mandatory.
© buildingSMART International – IDS User Manual (GitHub), CC BY-ND 4.0.

## Slide 31: IDS Structure | Cardinality
Applicability
An object according to the determined applicability must not exist For example: IfcBuildingElementProxy.Notdefined objects not allowed in the model.
© buildingSMART International – IDS User Manual (GitHub), CC BY-ND 4.0.

## Slide 32: IDS Structure | Cardinality
Requirements
Property must be filled in according to the requirement For example: Each IfcWall element must have a PredefinedType
© buildingSMART International – IDS User Manual (GitHub), CC BY-ND 4.0.

## Slide 33: IDS Structure | Cardinality
Requirements
Property may not be filled in according to the requirement For example: An architectural model must not contain IfcWall elements with LoadBearing = TRUE
© buildingSMART International – IDS User Manual (GitHub), CC BY-ND 4.0.

## Slide 34: IDS Structure | Cardinality
Requirements
Property may be empty, if filled in this is according to the requirement For example: An IfcWall may have a FireRating property.
© buildingSMART International – IDS User Manual (GitHub), CC BY-ND 4.0.

## Slide 35: Blender 5.0 – Bonsai BIM
User interface
      outliner (left)
      3D viewport (center)
      properties (bonsai add-on)
1
2
3

## Slide 36: Blender 5.0 – Bonsai BIM
View & Navigatie
      Open the model from the course material
      Set up Navigation Preferences & Spacebar Preference

## Slide 37: Blender 5.0 – Bonsai BIM
Shortcuts
      Use Shift + B to zoom and draw the view you want to zoom in on
      Click on an object and use the period '.' on your numpad to zoom to an object
      Use Shift + Right-Click to define a new orbit focus point
      Use Shift + H to isolate objects
      Use Alt + H to unhide all objects
      Use Shift + C to center selected
      Use Alt + B to define a clipping region (or to undo a clipping region)

## Slide 38: Blender 5.0 – Bonsai BIM
IDS Specifying
      Quality and coordination
      IFC tester
      Start IfcTester Webapp
1
2
3

## Slide 39: Blender 5.0 – Bonsai BIM
IDS Specifying
      Quality and coordination
      IFC tester
      Start IfcTester Webapp
      Go to Browser
      New IDS
4

## Slide 40: Blender 5.0 – Bonsai BIM
IDS Specifying
      Quality and coordination
      IFC tester
      Start IfcTester Webapp
      Go to Browser
      New IDS
      New
      Create Specification
6
5

## Slide 41: Blender 5.0 – Bonsai BIM
IDS Specifying
      Quality and coordination
      IFC tester
      Start IfcTester Webapp
      Go to Browser
      New IDS
      New
      Create Specification

## Slide 42: Blender 5.0 – Bonsai BIM
Search Global ID
      Project Overview
      Grouping and Filtering
        Add Search Group
        Add Filter
        Fill in Global ID
        Search
      Shift + H
      Or use the Search bar
2
1

## Slide 43: Blender 5.0 – Bonsai BIM
Properties
      Object information
      Object metadata
2
1

## Slide 44: Solibri Model Checker
Show passed elements
1
2
3

## Slide 45: BIM Collab Zoom
1. Use the IDS Results Panel
      Run the IDS validation in BIMcollab Zoom.
      Open the IDS Results panel.
      Select a requirement in the results tree.
      At the top of the results list, change the result filter:
        Switch from Failed to Passed or All.
    This will display the elements that passed the rule.
2. Select Passed Elements in the Model
    Once the filter shows Passed:
      Click the result item.
      The passed elements will be selected/highlighted in the 3D view.
      You can isolate them if needed.

## Slide 46: Example IDS
    For all non-load-bearing walls, if the wall has a fire rating, this must be specified according to the European classification (EI30; EI60; EI120; …).
    The naming of these walls follows the structure: <element abbreviation >_<classification>_<description>
Specification applicability

## Slide 47: Example IDS
    For all non-load-bearing walls, if the wall has a fire rating, this must be specified according to the European classification (EI30; EI60; EI120; …).
    The naming of these walls follows the structure: <element abbreviation >_<classification>_<description>
Specification applicability
Facet = Entity

## Slide 48: Example IDS
    For all non-load-bearing walls, if the wall has a fire rerating, this must be specified according to the European classification (EI30; EI60; EI120; …).
    The naming of these walls follows the structure: <element abbreviation >_<classification>_<description>
    .
Specification applicability
Facet = Property

## Slide 50
Specification applicability

## Slide 51
Applicability Facets

## Slide 52: Example IDS
    For all non-load-bearing walls, if the wall has a fire rating, this must be specified according to the European classification (EI30; EI60; EI120; …).
    The naming of these walls follows the structure: <element abbreviation >_<classification>_<description>
Specification requirement
Specification requirement

## Slide 53: Example IDS
    For all non-load-bearing walls, if the wall has a fire rating, this must be specified according to the European classification (EI30; EI60; EI120; …).
    The naming of these walls follows the structure: <element abbreviation >_<classification>_<description>
Specification requirement
Facet = Property

## Slide 55: Example IDS
    For all non-load-bearing walls, if the wall has a fire rating, this must be specified according to the European classification (EI30; EI60; EI120; …).
    The naming of these walls follows the structure: <element abbreviation >_<classification>_<description>
Specification requirement
Facet = Attribute

## Slide 57
Specification Requirements

## Slide 58
Requirement Facets